# Broadly Reconfigurable and Expandable Automation Device (BREAD) – Slice Datasheet: Stepper Motor Control Slice (SLC-STEP)
By: Nicholas Whisman (ngwhisma@mtu.edu) – Revision 0, on 18. May 2021
## Short Device Description
This device is designed to very finely control up to four stepper motors. The system has a feedback path in the form of 4 analog inputs. Finer control can be achieved by utilizing the microstep pin connections.
## Quick Information
Device at a Glance
Short title	Stepper Motor Control Slice
Part #	SLC-STEP
Repository Link	Link to OSF or other repository
Academic Paper DOI	DOI link to published paper
Device Cost	Monetary cost of the device
Assembly Difficulty	Difficult, Millable
Application Area	Controls, Robotics

Device Connections
J2 – Analog Input Paths
Pin #	Description	Rating
1	Analog Input 1	5V
2	Analog Input 2	5V
3	Analog Input 3	5V
4	Analog Input 4	5V

J3 – Output to Stepper
Pin #	Description	Rating
1	Motor 2, Signal 1B	±2A
2	Motor 2, Signal 1A	±2A
3	Motor 2, Signal 2A	±2A
4	Motor 2, Signal 2B	±2A
5	Motor 1, Signal 1B	±2A
6	Motor 1, Signal 1A	±2A
7	Motor 1, Signal 2A	±2A
8	Motor 1, Signal 2B	±2A

J4 – Output to Stepper
Pin #	Description	Rating
1	Motor 3, Signal 2B	±2A
2	Motor 3, Signal 2A	±2A
3	Motor 3, Signal 1A	±2A
4	Motor 3, Signal 1B	±2A
5	Motor 4, Signal 2B	±2A
6	Motor 4, Signal 2A	±2A
7	Motor 4, Signal 1A	±2A
8	Motor 4, Signal 1B	±2A

## Commands
Set Up (no significant returns)
Byte: Address	Bit: 1	Float: Target Temp	Float: Ramp Rate (d/m)
Speed Select (no significant returns)
Byte: Address	Bit: 0	Float: 0	Float: 0
Step Select (no significant returns)

Analog Read (returns voltage on selected analog input line)

## Schematic

Figure 1: BREAD Connection Port and Power Capacitors

Figure 2: Arduino Nano

Figure 3: Custom Power Select

Figure 4: One of four breakout stepper motor drivers

Figure 5: One of four feedback voltage paths

Figure 6: Signal Input Ports

## Bill of Materials
Designator	Description	Quantity	Cost / part	URL
J5	01x03 1/10” Pitch Male Connector Pins	1	0.27	https://www.digikey.com/short/jv0b95z0
C1-3	1206 Packaging 10 µF Capacitor	3	0.64	https://www.digikey.com/short/qfrbqfhd
J6	01x02 1/10” Pitch Terminal Block	1	1.27	https://www.digikey.com/short/0v8hf4h8
R1-4	1k 1206 Packaging Resistor	4	0.10	https://www.digikey.com/short/wp8502p7
J3-4	01x08 1/10” Pitch Terminal Block	2	6.45	https://www.digikey.com/short/mqn9fd88
J2	01x04 1/10” Pitch Terminal Block	1	2.75	https://www.digikey.com/short/tv7tzq1r
D1-4	5.1V Zener Diode	4	0.22	https://www.digikey.com/short/z0f0ztp2
A1-4	Pololu A4988 Stepper Driver	4	5.95	https://www.pololu.com/category/156/a4988-stepper-motor-driver-carriers
G1	Arduino Nano	1	22.00	https://www.digikey.com/en/products/detail/arduino/A000005/2638989
J1	01x10 Female Header Pins	1	0.79	https://www.digikey.com/short/23bfwwjh

## Construction & Fabrication
List any tools that are required and short guide on the order which parts should be soldered / assembled. Be sure to note any specialized methods and point out components that may easily be soldered in the incorrect orientation. Additionally include at least one picture of the assembled board (include both sides if there are components on both sides).
[Image of the assembled Circuit Board]
Fig #. Subtitle should go here.
## Configuration & Calibration
Include a list of default jumper and potentiometer positions:
Hardware Positions
- Turn P1 to be roughly 50%
- Turn P2 to be completely closed (turn clockwise until potentiometer clicks)
- Place a jumper to short out J3. Etc…
Detail any key parameters the end-user may want to adjust in the firmware, and if there are any special instructions before programming the Slice.
Tools Required For Calibration
- An oscilloscope with at least 15Mhz sampling
- A multimeter. Etc…
List all of the tools / instruments required for calibration. Provide a detailed & step by step guide on how to calibrate (or validate) each unique type of channel on the card. Include what variables in the firmware may need to be adjusted (and when). Attach a wiring diagram for each relevant calibration circuit.
[Image of the calibration circuit]
Fig #. Subtitle should go here.
## Usage & Constraints
List the relevant constraints for each type of channel on the card. These parameters may be quantities like max current, max voltage, frequency, sampling frequency, etc.
List an example wiring diagram of the slice in use, as well as some suggested applications
[Image of the example usage wiring diagram]
Fig #. Subtitle should go here.
## General Comments on Slice
This section is intended as a catch-all for any topics that are relevant to the Slice that don’t fit in any other category.
## Revision Notes
Rev 0 – Initial document release (DATE HERE)